## Slide 1: Designing a 4-bit ALU
COMPUTER ORGANIZATION · DIGITAL LOGIC
AND, OR and Set-Less-Than (SLT), selected by a multiplexer — design, working and applications
Presented by:
M. Shiva Sai- 2620030194
C. Bhargav Karthik-2620030188
D. Manvitha-2620030178
C. Ramya Sree-2620030230
A = 0101
B = 0110
Op = 11
Notes: Introduce the topic: we design a 4-bit Arithmetic Logic Unit that performs three operations — bitwise AND, bitwise OR and Set-Less-Than — with a multiplexer choosing which result appears at the output.

## Slide 2: What the ALU does
01 · INTRODUCTION
The Arithmetic Logic Unit is the combinational heart of a CPU: it takes two 4-bit operands, A and B, computes several results in parallel, and a multiplexer picks the one requested by the operation-select lines.
&
AND
Bitwise: each result bit is 1 only when both input bits are 1.
0101 AND 0110 = 0100
|
OR
Bitwise: each result bit is 1 when either input bit is 1.
0101 OR 0110 = 0111
<
SLT
Set-Less-Than: result is 0001 if A < B (signed), otherwise 0000.
5 < 6 → 0001
Notes: AND and OR are pure logic, done bit by bit. SLT is a comparison: it needs a subtraction A − B internally, then looks at the sign. All three are computed at the same time; the multiplexer just chooses which one to output.

## Slide 3: The 1-bit ALU slice
02 · DESIGN
Each bit position has its own slice. An AND gate, an OR gate and a full adder all work on inputs a and b at once.
Binvert feeds b̄ to the adder so it computes a − b for SLT.
A 4-to-1 MUX with a 2-bit select chooses which signal becomes the slice's result.
a, b
AND
OR
Adder
a + b̄ + Cin
Less (in)
0
1
2
3
MUX
4:1
Result
Op select [1:0]
Notes: Walk through the slice: both inputs go to all three units at once. The mux inputs are numbered 0 to 3 — AND on 0, OR on 1, the adder sum on 2 (used internally), and the Less signal on 3. The 2-bit Operation select decides which one leaves as the result. The adder also produces CarryOut, which ripples to the next slice.

## Slide 4: Chaining four slices into a 4-bit ALU
02 · DESIGN
Carries ripple from bit 0 to bit 3, and Op select and Binvert reach every slice. For SLT, CarryIn0 = 1 so the adders compute A − B.
a3 b3
ALU 3
Less = 0
produces Set
R3
a2 b2
ALU 2
Less = 0
R2
a1 b1
ALU 1
Less = 0
R1
a0 b0
ALU 0
Less = Set
R0
Cin0
Set = sign bit of A − B, fed back to the Less input of bit 0
Notes: Point out the ripple carry in blue and the feedback in orange. Only the most significant slice knows the sign of A − B. That Set signal goes back to bit 0's Less input; the other three Less inputs are tied to 0. So when SLT is selected the output is 000 followed by the sign bit — 0001 if A is less than B. For full correctness with overflow, Set is sign XOR overflow.

## Slide 5: How the select lines drive each operation
03 · WORKING
Operation | Binvert | Op[1:0] | Output
AND | 0 | 00 | A AND B
OR | 0 | 01 | A OR B
SLT | 1 | 11 | 0001 if A < B, else 0000
For SLT, Binvert = 1 and CarryIn0 = 1 make every adder compute A + B̄ + 1 = A − B. The MUX in each slice passes its Less input, so only bit 0 can be 1.
Worked example
A = 0101 (5)
B = 0110 (6)
AND → 0100
OR → 0111
SLT: 0101 + 1001 + 1
= 1111 → sign 1
SLT → 0001 (5 < 6)
Notes: Read the table row by row. Then trace the example: AND keeps only the shared 1 in bit 2, OR combines them. For SLT, B is inverted to 1001 and 1 is added, giving 1111, which is −1 in two's complement. The sign bit is 1, so Set = 1 and the ALU outputs 0001, meaning A is less than B.

## Slide 6: Where this ALU is used
04 · APPLICATIONS
CPU instructions
Implements MIPS/RISC-V and, or and slt; slt plus a branch gives if (a < b) decisions.
Bit masking
AND clears or tests bits; OR sets flags in control and status registers.
Comparison & sorting
SLT finds min/max values and drives sorting in embedded and DSP chips.
Scalable building block
The same slice repeats to build 8-, 16- or 32-bit ALUs in FPGAs and processors.
Notes: Close the technical part with real uses. The key message: the mux-based slice design is modular, so a 4-bit ALU scales to 32 bits just by adding slices, and SLT is exactly how processors implement less-than comparisons.

## Slide 7
SLT(you, questions) = 0001
Thank You
Questions?
Notes: Thank the audience and invite questions.