## Slide 1
01011010 00110101 11001010 01011101 00101101 10101100 01011010
10100101 01101011 00011010 10110101 01011010 11010101 00101101
11010010 01011010 00110101 11001010 01011101 00101101 10101100
01011010 10100101 01101011 00011010 10110101 01011010 11010101
1
0
0
0
0
1
0
1
DIGITAL LOGIC DESIGN
Design and Simulation of
8-Bit Signed Binary Number Representation
Using the Sign-Magnitude Method
BY TEAM MEMBERS:
2620030230_Ramya Sree
2620030178_Manvitha
2620030188_Bhargav Karthik
2620030194_Shiva Sai
A study of representing and simulating positive & negative integers
within an 8-bit binary word

## Slide 2
Introduction & Objective
Digital systems store everything — including negative numbers — as bits. Since plain binary only expresses magnitude, a dedicated scheme is needed to also encode the sign of a value. The Sign-Magnitude method is the most intuitive of these schemes, closely mirroring how humans write signed numbers on paper (a ‘+’ or ‘–’ followed by the value).
1
Represent
Encode both positive and negative integers within a fixed 8-bit word.
2
Design
Define the sign-magnitude bit structure and its encoding/decoding rules.
3
Simulate
Model the scheme in software/logic to verify range, zero cases and arithmetic.
AN 8-BIT WORD
1
Sign
0
2^6
1
2^5
0
2^4
1
2^3
1
2^2
0
2^1
1
2^0
MSB = Sign Bit
0 = Positive 1 = Negative
Remaining 7 Bits
Represent the Magnitude
“One bit for sign, the rest for value —
closes the gap between binary and
everyday signed notation.”
02
8-BIT SIGN-MAGNITUDE REPRESENTATION

## Slide 3
Ways to Represent Signed Numbers
Three common binary schemes — this project focuses on the first
FOCUS OF THIS DECK
Sign-Magnitude
MSB stores the sign (0/1); remaining bits store the magnitude, unchanged from unsigned binary.
-5 → 1 0000101
1’s Complement
Negative numbers formed by inverting every bit of the positive value.
-5 → 1 1111010
2’s Complement
Negative numbers formed by inverting all bits, then adding 1. Used in most real hardware.
-5 → 1 1111011
03
8-BIT SIGN-MAGNITUDE REPRESENTATION

## Slide 4
Structure of the Sign-Magnitude Format
S
SIGN
M
2^6
M
2^5
M
2^4
M
2^3
M
2^2
M
2^1
M
2^0
Bit 7
(Sign
Bit)
Bits 6 – 0
7-bit Magnitude Field — same value as ordinary unsigned binary
0
Sign Bit = 0
The value is positive.
Example: 0 0000101 = +5
1
Sign Bit = 1
The value is negative.
Example: 1 0000101 = –5
General form: N = (–1)^SIGN × |Magnitude|, where the sign bit selects the exponent of –1
04
8-BIT SIGN-MAGNITUDE REPRESENTATION

## Slide 6
Encoding Examples
Decimal values converted into 8-bit sign-magnitude form
Decimal | Sign | Magnitude (7 bits) | 8-bit Sign-Magnitude | Note
+5 | 0 | 0000101 | 0 0000101 | positive
–5 | 1 | 0000101 | 1 0000101 | negative
+127 | 0 | 1111111 | 0 1111111 | max positive
–127 | 1 | 1111111 | 1 1111111 | max negative
+0 | 0 | 0000000 | 0 0000000 | zero (positive)
–0 | 1 | 0000000 | 1 0000000 | zero (negative)
Notice: +0 and –0 have two different bit patterns for the same value — a key quirk of this method (see next slide).
05
8-BIT SIGN-MAGNITUDE REPRESENTATION

## Slide 7
+5
-5
+127
-127

## Slide 8
Range and Special Cases
What 8 bits can and cannot cleanly express
7
magnitude bits
available for value
–127 to +127
representable
decimal range
256
total bit patterns,
only 255 distinct values
The Duplicate-Zero Problem
0
0
0
0
0
0
0
0
= +0
1
0
0
0
0
0
0
0
= –0
Two encodings map to the same value, wasting a bit pattern and
complicating equality checks in simulation.
Symmetric Range
–127
0 / –0
+127
Unlike 2’s complement (–128 to +127), sign-magnitude is
perfectly symmetric — at the cost of the duplicate zero above.
06
8-BIT SIGN-MAGNITUDE REPRESENTATION

## Slide 9
Simulating Sign-Magnitude Arithmetic
Unlike 2’s complement, sign-magnitude cannot simply add bit patterns — the simulation logic must branch on the operand signs before performing magnitude arithmetic.
1
Read Signs
Extract the MSB of both operands to identify each number’s sign.
→
2
Compare Signs
If signs match, add the magnitudes and keep the common sign.
→
3
Subtract if Differ
If signs differ, subtract the smaller magnitude from the larger.
→
4
Assign Result Sign
Result takes the sign of the operand with the larger magnitude.
→
5
Check Overflow
Flag overflow if the magnitude result exceeds 7-bit capacity (127).
WORKED EXAMPLE
(+5) + (–3): signs differ → subtract magnitudes 5 – 3 = 2 → sign of larger magnitude (+5) is positive → result = +2
0 0000101 + 1 0000011 → 0 0000010
07
8-BIT SIGN-MAGNITUDE REPRESENTATION

## Slide 10
Advantages, Limitations & Conclusion
Advantages
✓
Simple, intuitive mapping to sign + value notation
✓
Symmetric range: equal count of positive & negative values
✓
Easy manual conversion between decimal and binary
✓
Sign bit is trivially isolated by reading the MSB
Limitations
✗
Two representations of zero (+0 and –0)
✗
Addition/subtraction needs conditional sign logic, not direct bit addition
✗
Hardware adders are more complex than 2’s complement designs
✗
Rarely used in real processors — mainly educational value
Conclusion
The sign-magnitude method offers a clear, human-readable foundation for understanding signed binary representation. Simulation confirms its correct range (–127 to +127) and highlights the practical issues — duplicate zero and added arithmetic complexity — that led modern hardware to adopt 2’s complement instead.
08
8-BIT SIGN-MAGNITUDE REPRESENTATION

## Slide 11
Thank
you!